Lithium-ion battery
recycling

Several factors contribute to making Li-ion battery recycling more complicated than Pb–acid or Ni–MH recycling. First, Li-ion batteries have a wider variety of materials in each cell. The active materials are in the form of powder, coated onto metal foil, and these different materials must be separated from each other during recycling. Lead–acid batteries have a relatively small number of large lead plates packed together in a single plastic case, while a Li-ion pack is likely to have 100 or more individual cells (~5000 for a Tesla electric vehicle), which are connected into modules and, in turn, are assembled into a pack with control circuitry attached to each cell. A thermal management system may also be included. These components could possibly be recovered intact or may contain valuable materials that would provide some economic incentive for recycling the battery pack.
With in the cells, the chemical compositions of the active materials – especially the cathode – vary with manufacturer and battery function, are changing, and may never standardize. The most common cathode material for the batteries now prevalent in consumer electronics is LiCoO2 (LCO), but various combinations of Ni, Mn, and Al can be used to replace some or all of the cobalt to optimize performance while lowering raw material cost, which is the key for automotive batteries. Another promising cathode material that uses very low cost inputs is LiFePO4 (LFP). Most manufacturers use some form of graphite for the anode, but silicon is also being used, and other materials and mixtures are being studied.
Lead–acid batteries are small and easily removed from their location under the hood, while the larger, more complex Li-ion packs vary in shape and location in the vehicle. As a result, removal may be more difficult. However, if removal takes a professional, fewer people need to be trained on proper handling and separation. If Li-ion batteries last the entire vehicle life, they will all end up in scrap yards or at auto dealers. These are both sufficiently large enterprises to facilitate collection.
Vehicle batteries subsequently used for stationary energy storage could be collected from utilities after this second use; collection from homes or smaller commercial installations would be more difficult.
At present, there are no regulations regarding recycling of large format Li-ion batteries. This condition might be thought to be good for recyclers, who would face no restrictions in process design. However, they would face the significant possibility that restrictive regulations could be imposed after the fact. Therefore, processes must be designed to be compliant with anticipated regulations. In addition, battery technology is still evolving. Recycling processes designed for a specific design or chemistry could become irrelevant quickly.
Automotive Li-ion batteries have only been in commercial use for about 5 years, and it will take some time until they are used in large volumes. And with their long product life (ideally, the life of the car), not nearly enough batteries have reached the end of their lives to support large-scale recycling plants. However, lithium batteries from consumer electronics, as well as processing scrap, are available and could supply feedstock for the fledgling recycling industry for automotive Li-ion batteries. Several recycling methods have been proposed, each with its advantages and disadvantages, as discussed below.